## Slide 1
Hugh Dillon, Zac Hawkins, Rick Holloway, Ben Smith, Hunter Thorington
MailBird

## Slide 2: OVERVIEW
Flight mode control
MAVlink Communication
I2C and SPI Communication
Triangulation Algorithm

## Slide 3: Flight mode control
Created new Roll/Pitch mode
  Sets IR flag to switch between GPS and camera error.
  Updates roll/pitch controller based on calculated roll/pitch from loiter controller.
Loiter controller called at 10Hz rate
  Updates nav_roll and nav_pitch based on camera error.

## Slide 4: MAVlink communication
A communication protocol used in small, remote vehicles.
Used for communications over telemetry or USB
Used by Mailbird to set flight mode from flight plan or long-range communication
Primary uses:
  Setting the flight mode from software
  Testing purposes – pymavlink, behavior patterns

## Slide 5: I2c
Inter Integrated Circuit Communications (I2C)
  Multiple addressing. single master – multiple slaves
  Repeated starts
  Register initialization

## Slide 6: The backup plan
Serial Peripheral Interface (SPI) – Backup plan
  No addressing: single master – single slave
Testing on Arduino Duemilanove and Uno

## Slide 7: IR Camera Printed Circuit Board
Smaller
More reliable
Mounting Holes

## Slide 8: Triangulation Algorithm
The triangulation algorithm allows the quad copter to determine its position over a landing pad with IR LEDs imbedded. The algorithm takes a set of two X,Y positions as inputs and outputs the quad copters x,y offset and elevation. The algorithm runs on the APM board in a 100Hz loop.

## Slide 10: Potential problems
Infrared White-out
Carrying Capacity
Viewing Angles
Simulation/Testing area
Weather

## Slide 11: Budget
Total budget of $50 per team member
Estimated costs: ~$225
Unexpected costs: ~$25

## Slide 12: timeline
Proposal: January 22
Cycle 1: March 6
  Working control algorithm
Cycle 2: April 25
  Final design report by April 18
  Senior Design Fair: April 25